## Slide 1: CS654: Digital Image Analysis
Lecture 25: Hough Transform
Slide credits: Guillermo Sapiro, Mubarak Shah, Derek Hoiem

## Slide 2: Recap of Lecture 24
Introduction to image segmentation
Top down and bottom up segmentation
Edge based segmentation
First order derivative operators
Second order derivative operator
DoG, LoG

## Slide 3: Outline of Lecture 25
Preprocessing Edge Images
Edge Tracking Methods
Fitting Lines and Curves to Edges
The Hough Transform

## Slide 4: Boundaries of Objects
Marked by many users
http://www.eecs.berkeley.edu/Research/Projects/CS/vision/grouping/segbench/bench/html/images.html

## Slide 5: Boundaries of Objects from Edges
Brightness Gradient (Edge detection)
Missing edge continuity, many spurious edges

## Slide 6: Boundaries of Objects from Edges
Multi-scale Brightness Gradient
But, low strength edges may be very important

## Slide 7: Boundaries of Objects from Edges
Image
Machine Edge Detection
Human Boundary Marking

## Slide 8: Boundaries in Medical Imaging
Detection of cancerous regions.
[Foran, Comaniciu, Meer, Goodell, 00]

## Slide 9: Boundaries in Ultrasound Images
Hard to detect in the presence of large amount of speckle noise

## Slide 10: Boundaries of Objects
Sometimes hard even for humans!

## Slide 11: Preprocessing Edge Images
Image
Edge detection
and Thresholding
Noisy edge image
Incomplete boundaries
Shrink and Expand
Thinning

## Slide 12: How to fit a line
Least squares Fit (over constraint)
  There are more equations than unknowns
  Many points two unknowns
RANSAC (constraint)
  Number of equations are equal to the number of unknowns
  Two points, one line
Hough Transform (under constraint)
  There are fewer equations than unknowns
  One equation, two unknowns

## Slide 13: Fitting Lines to Edges (Least Squares)
Given: Many pairs
Find: Parameters
Minimize: Average square distance:

## Slide 14: Fitting Lines to Edges (Least Squares)
Minimize: Average square distance:
Using:
Note:

## Slide 15: Curve Fitting
Find Polynomial:
that best fits the given points
Minimize:
Using:
Note: is LINEAR in the parameters (a, b, c, d)

## Slide 16: RANSAC (Random Sampling and Consensus)
Randomly select two points to fit a line
Find the error between the estimated solution and all other points.
If the error is less than tolerance, then quit, else go to step (1).

## Slide 17: Line Grouping Problem
Slide credit: David Jacobs

## Slide 18: This is difficult because of:
Extraneous data: clutter or multiple models
  We do not know what is part of the model?
  Can we pull out models with a few parts from much larger amounts of background clutter?
Missing data: only some parts of model are present
Noise
Cost:
  It is not feasible to check all combinations of features by fitting a model to each possible subset

## Slide 19: Hough Transform
Elegant method for direct object recognition
    Edges need not be connected
    Complete object need not be visible
    Key Idea: Edges VOTE for the possible model
Several Lines
• How do we Know which points belong to
which lines?

## Slide 20: Line Fitting: Hough Transform
Line equation
Rewrite this equation
For particular edge pointthis becomes
This is an equation of a line in space

## Slide 21: Image and Parameter Spaces
Equation of Line:
Find:
Consider point:
Image Space
Parameter Space
Parameter space also called
Hough Space

## Slide 22: Line Detection by Hough Transform
Parameter Space
 | 1 |  |  |  |  |  | 1 |  | 
 |  | 1 |  |  |  | 1 |  |  | 
 |  |  | 1 |  | 1 |  |  |  | 
 |  |  |  | 2 |  |  |  |  | 
 |  |  | 1 |  | 1 |  |  |  | 
 |  | 1 |  |  |  | 1 |  |  | 
 | 1 |  |  |  |  |  | 1 |  | 
Algorithm:
Quantize Parameter Space
Create Accumulator Array
Set
For each image edge increment:
If lies on the line:
Find local maxima in

## Slide 23: Better Parameterization
NOTE:
Large Accumulator
More memory and computations
Improvement:
Line equation:
Here
Given points find
(Finite Accumulator Array Size)
Image Space
Hough Space
?
Hough Space Sinusoid

## Slide 24
Image space
Votes
Horizontal axis is θ, vertical is rho.
Notes: Figure 15.1, top half. Note that most points in the vote array are very dark, because they
get only one vote.

## Slide 25
Image space
votes
Notes: This is 15.1 lower half

## Slide 26
Image space
votes
Notes: 15.2; main point is that lots of noise can lead to large peaks in the array

## Slide 27
Fewer votes land in a single bin when noise increases.
Notes: This is the number of votes that the real line of 20 points gets with increasing noise (figure15.3)

## Slide 28
Adding more clutter increases number of bins with false peaks.
Notes: Figure 15.4; as the noise increases in a picture without a line, the number of points in the max cell goes
up, too

## Slide 29
Mechanics of the Hough transform
Difficulties
  how big should the cells be?
  too big, and we merge quite different lines;
  too small, and noise causes lines to be missed)
How many lines?
  Count the peaks in the Hough array
  Treat adjacent peaks as a single peak
Which points belong to each line?
  Search for points close to the line
  Solve again for line and iterate

## Slide 30: Real World Example
Original
Edge Detection
Found Lines
Parameter Space

## Slide 31: Finding Circles by Hough Transform
Equation of Circle:
If radius is known:
Accumulator Array
(2D Hough Space)
Image space

## Slide 32: Finding Circles by Hough Transform
Equation of Circle:
Image space
Hough Space
If radius is known:
Accumulator Array
(2D Hough Space)

## Slide 33: Finding Circles by Hough Transform
Equation of Circle:
If radius is not known: 3D Hough Space!
Use Accumulator array
What is the surface in the Hough space?
Image space

## Slide 34: Using Gradient Information
Gradient information can save lot of computation:
Edge Location
Edge Direction
Need to increment only one point in Accumulator!!
Assume radius is known:

## Slide 35: Finding Coins
Original
Edges (note noise)

## Slide 36: Finding Coins (Continued)
Pennies
Quarters

## Slide 37: Finding Coins (Continued)
Coin finding sample images from: Vivek Kwatra
Note that because the quarters and penny are different sizes, a different Hough transform (with separate accumulators) was used for each circle size.

## Slide 38: Generalized Hough Transform
Model Shape NOT described by equation
Requires training
  Object of known shape
  Generate model
R-table
Similar approach to line and circle fitting during detection

## Slide 39: Generating R Table
Compute centroid
For each pixel compute r
Find edge orientation
Construct a table of angle and r values

## Slide 40: Generating R-table
Edge orientation | Distance (r)
Edge orientation | Distance (r)

## Slide 41: GHT Algorithm
Quantize the parameter space
For each edge point do
Find the local maxima in the parametric space
Compute
For each table entry for do

## Slide 42: Scale and Rotation Invariance
Rotation angle =
Scale along x=
Scale along y=
Modified centroid location
Transformed coordinate

## Slide 43: Hough Transform: Comments
Works on Disconnected Edges
Relatively insensitive to occlusion
Effective for simple shapes (lines, circles, etc)
Trade-off between work in Image Space and Parameter Space
Handling inaccurate edge locations:
    Increment Patch in Accumulator rather than a single point

## Slide 44: Thank you
Next Lecture: Region based segmentation